INTERNET ROBOTARM CONTROLLER
Version 0.1 alpha

Rein Velt
5 januari 2009

This is a work in progress.

# Introduction

This document describes how to control your Lynxmotion robotarm from the internet.

# The Robotarm

We used the Lynxmotion AL5D Robotic Arm Combo Kit as base for our robotarm. You can also use the cheaper robotarm models from Lynxmotion because the controller uses the same protocol. The arm has the following features:

- Serial port-based version with powerful PC software.
- Includes RIOS, a powerful interactive Windows program that uses external inputs to affect the robot's motion in closed-loop projects.
- Advanced inverse kinematics positioning control using mouse or joystick.
- Easily control from a Bot Board with Basic Atom or Basic Stamp 2, with the new BASIC code export function.
- This product includes everything you need to control the arm from a personal computer.

More information:
http://www.lynxmotion.com/Product.aspx?productID=675&CategoryID=130

# Controller

The controller uses the rs232 serial protocol for the communication. You can connect the controller to a microcontroller (Arduino, AVR, PIC, Basicstamp) or you can control it from a webserver using DIO (Direct I/O) commands.

## PHP Web Controller
This section contains the sourcecode to control the robotarm with PHP. You don't need an Arduino controller for this example. PHP can communicate directly with the RS232 interface at the LynxMotion controller. More information about DIO can be found at http://php.net/manual/en/book.dio.php

<php

//This example uses the php direction i/o extension to control the
//the lynxmotion robotarm using the pololu protocol

class robotArm
{

public function put($servo, $angle)
{
 //the put function uses pololu mode command 4 to set absolute position
 //servo is the servo number (typically 0-7)
 //angle is the absolute position from 500 to 5500

  $temp = $angle & 0x1f80; //get bits 8 thru 13 of position
  $pos_hi = temp >> 7; //shift bits 8 thru 13 by 7
  $pos_low = $angle & 0x7f; //get lower 7 bits of position

  dio_write(0x80,1); //start byte
  dio_write(0x01,1); //device id
  dio_write(0x04,1); //command number
  dio_write($servo,1); //servo number
  dio_write($pos_hi, 1); //bits 8 thru 13
  dio_write($pos_low, 1); //bottom 7 bits
}

public function set_speed($servo, $speedVal)
{
  //servo is the servo number (typically 0-7)
  //speedVal is servo speed (1=slowest, 127=fastest, 0=full)
  //set speedVal to zero to turn off speed limiting

  $speedVal = $speedVal & 0x7f; //take only lower 7 bits of the speed

  //Send a Pololu Protocol command
  dio_write(0x80,1); //start byte
  dio_write(0x01,1); //device id
  dio_write(0x01,1); //command number
  dio_write(servo,1); //servo number
  dio_write(speedVal,1); //speed
}

public function grip_open()
{
 $this->put(4, 4260);
}

public function grip_close()
{
 $this->put(4, 1550);
}

?>
## Arduino Controller firmware
This section contains the sourcecode for the Arduino microcontroller to communicate with the robot arm. Some potmeters and leds are connected to the Arduino. The joints can be controlled with the potmeters.

// Robot arm joint positioner
// Software Serial from Arduino example by Tom Igoe
// put() & set_speed() functions found on pololu forums & modified
// mike crist 2009-01-02

#include <SoftwareSerial.h>

#define rxPin 2
#define txPin 3
#define gripSwitch 4
#define upSwitch 5
#define downSwitch 6
#define gripLED 7
#define wristLED 8
#define elbowLED 9
#define shoulderLED 10
#define baseLED 11
#define potPin 0
#define baseServo 0
#define shoulderServo 1
#define elbowServo 2
#define wristServo 3
#define gripServo 4

int wristVal = 3050;
int elbowVal = 2400;
int shoulderVal = 1880;
int baseVal = 3000;
int gripVal = 1550;
int mode = 1;

// set up a new serial port
SoftwareSerial mySerial = SoftwareSerial(rxPin, txPin);

void setup()
{
  pinMode(rxPin, INPUT);
  digitalWrite(txPin, HIGH); // keeps pololu board from getting spurious signal
  pinMode(txPin, OUTPUT);
  pinMode(gripSwitch, INPUT);
  pinMode(upSwitch, INPUT);
  pinMode(downSwitch, INPUT);
  pinMode(gripLED, OUTPUT);
  pinMode(wristLED, OUTPUT);
  pinMode(elbowLED, OUTPUT);
  pinMode(shoulderLED, OUTPUT);
  pinMode(baseLED, OUTPUT);
  // set the data rate for the hardware serial port
  Serial.begin(9600);
  // set the data rate for the SoftwareSerial port
  mySerial.begin(9600);
  set_speed(0, 15);
  set_speed(1, 10);
  set_speed(2, 15);
  set_speed(3, 55);
  set_speed(4, 127);
  put(baseServo, baseVal);
  put(shoulderServo, shoulderVal);
  put(elbowServo, elbowVal);
  put(wristServo, wristVal);
  put(gripServo, gripVal);
}

void loop()
{
  // mode is set by up and down button switches
  // mode 1 is base adjust thru mode 5 gripper adjust

  if(digitalRead(upSwitch) == HIGH) // if the up switch is pressed
  {
    mode++;
    if(mode == 6){mode = 1;}
  }
  if(digitalRead(downSwitch) == HIGH) // if the down switch is pressed
  {
    mode--;
    if(mode == 0){mode = 5;}
  }

  switch (mode)
  {
    case 1: //base adjust mode
        digitalWrite(baseLED, HIGH);
        digitalWrite(shoulderLED, LOW);
        digitalWrite(elbowLED, LOW);
        digitalWrite(wristLED, LOW);
        digitalWrite(gripLED, LOW);
        baseVal = readPot(1145, 4800);
        put(baseServo, baseVal);
        break;
    case 2: //shoulder adjust mode
        digitalWrite(baseLED, LOW);
        digitalWrite(shoulderLED, HIGH);
        digitalWrite(elbowLED, LOW);
        digitalWrite(wristLED, LOW);
        digitalWrite(gripLED, LOW);
        shoulderVal = readPot(1145, 3000);
        put(shoulderServo, shoulderVal);
        break;
    case 3: //elbow adjust mode
        digitalWrite(baseLED, LOW);
        digitalWrite(shoulderLED, LOW);
        digitalWrite(elbowLED, HIGH);
        digitalWrite(wristLED, LOW);
        digitalWrite(gripLED, LOW);
        elbowVal = readPot(1570, 3340);
        put(elbowServo, elbowVal);
        break;
    case 4: //wrist adjust mode
        digitalWrite(baseLED, LOW);
        digitalWrite(shoulderLED, LOW);
        digitalWrite(elbowLED, LOW);
        digitalWrite(wristLED, HIGH);
        digitalWrite(gripLED, LOW);
        wristVal = readPot(1275, 4760);
        put(wristServo, wristVal);
        break;
    case 5: //gripper adjust mode
        digitalWrite(baseLED, LOW);
        digitalWrite(shoulderLED, LOW);
        digitalWrite(elbowLED, LOW);
        digitalWrite(wristLED, LOW);
        digitalWrite(gripLED, HIGH);
        gripVal = readPot(1550, 4750);
        put(gripServo, gripVal);
  }

  printOut();
  //delay(100);
}

void put(int servo, int angle)
{
  //the put function uses pololu mode command 4 to set absolute position
  //servo is the servo number (typically 0-7)
  //angle is the absolute position from 500 to 5500

   unsigned int temp;
   byte pos_hi,pos_low;

   temp = angle & 0x1f80; //get bits 8 thru 13 of position
   pos_hi = temp >> 7; //shift bits 8 thru 13 by 7
   pos_low = angle & 0x7f; //get lower 7 bits of position

   mySerial.print(0x80,BYTE); //start byte
   mySerial.print(0x01,BYTE); //device id
   mySerial.print(0x04,BYTE); //command number
   mySerial.print(servo,BYTE); //servo number
   mySerial.print(pos_hi, BYTE); //bits 8 thru 13
   mySerial.print(pos_low, BYTE); //bottom 7 bits
}

void set_speed(byte servo, byte speedVal)
{
   //servo is the servo number (typically 0-7)
   //speedVal is servo speed (1=slowest, 127=fastest, 0=full)
   //set speedVal to zero to turn off speed limiting

   speedVal = speedVal & 0x7f; //take only lower 7 bits of the speed

   //Send a Pololu Protocol command
   mySerial.print(0x80,BYTE); //start byte
   mySerial.print(0x01,BYTE); //device id
   mySerial.print(0x01,BYTE); //command number
   mySerial.print(servo,BYTE); //servo number
   mySerial.print(speedVal,BYTE); //speed
}

void grip_open()
{
  put(4, 4260);
}

void grip_close()
{
  put(4, 1550);
}

int readPot(int lowNum, int highNum)
{
  int potVal = analogRead(potPin);
  potVal = map(potVal, 0, 1023, lowNum, highNum);
  return potVal;
}

void printOut()
{
  Serial.print("gripper = ");
  Serial.print(gripVal);
  Serial.print(" wrist = ");
  Serial.print(wristVal);
  Serial.print(" elbow = ");
  Serial.print(elbowVal);
  Serial.print(" shoulder = ");
  Serial.print(shoulderVal);
  Serial.print(" base = ");
  Serial.println(baseVal);
}